## Slide 1: HAZCOM 2012 Worker Training

## Slide 2: Occupational Safety and Health Administration – OSHA “HAZCOM 2012”: new OSHA rules to conform with the… Globally Harmonized System – GHS Worker Training Due December 1, 2013

## Slide 3: This is “one-time” training. No periodic, refresher training is required. No test or training certificate is required. However, a “Certificate of Training” is provided here (last slide). Should be placed in employees’ files. Make as many copies as needed for the number of trainees.

## Slide 4: Training: Two Major Parts I. Hazard Labels on Chemical Containers II. Safety Data Sheets (SDSs) formerly “Material Safety Data Sheets”

## Slide 5: Chemical manufacturers and importers are required to evaluate the hazards of the chemicals they produce or import, and prepare Labels and Safety Data Sheets to convey the hazard information to their downstream customers. All employers with hazardous chemicals in their workplaces must have Labels and Safety Data Sheets for their exposed workers, and train them to handle the chemicals appropriately.

## Slide 6: June 1, 2015 (or Before) Labels: New GHS Standard Format and GHS Pictograms on Labels
I. Labels

## Slide 7
Hazard Labels Appear on Containers Encountered in the Workplace

## Slide 8: A “GHS label” must Include: Product Identifier e.g., Chemical Name Signal Word “Danger” or “Warning” Pictograms see following slides Hazard Statement e.g., “Causes irritation….” Precautionary Statement “Keep away from….” “In case of exposure…” Supplier’s Name, Address, Phone#

## Slide 9: The Following Slides Include: The Pictogram's Name & The Chemical’s Hazard Classifications

## Slide 10: Flame
• Flammables
• Pyrophorics
• Self-Heating
• Emits Flammable Gas
• Self-Reactives
• Organic Peroxide

## Slide 11: Flame Over Circle
• Oxidizers

## Slide 12: Exploding Bomb
• Explosives
• Self-Reactives
• Organic Peroxide

## Slide 13: Skull and Crossbones
• Acute Toxicity
(fatal or toxic)

## Slide 14: Corrosion
• Skin Corrosion / Burns
• Eye Damage
• Corrosive to Metal

## Slide 15: Gas Cylinder
• Gases Under Pressure

## Slide 16: Health Hazard
• Carcinogen • Mutagenicity • Reproductive Toxicity • Respiratory Sensitizer • Target Organ Toxicity
• Aspiration Toxicity

## Slide 17: Exclamation Mark
• Irritant (skin and eye)
• Skin Sensitizer
• Acute Toxicity (harmful)
• Narcotic Effects
• Respiratory Tract
Irritant
• Hazardous to Ozone
Layer (Non-Mandatory)

## Slide 18: Environment (It is optional to apply this label)
• Aquatic Toxicity

## Slide 20: II. Safety Data Sheets
Formerly called Material Safety Data Sheets (MSDS)
To be accessed by workers in the event of a chemical exposure or chemical release emergency.

## Slide 21: June 1, 2015 (or before) A new, uniform 16-section format All SDS’s must follow this format

## Slide 22: SDS Sections 1. Identification 2. Hazard(s) identification 3. Composition/information on ingredients 4. First-aid measures 5. Fire-fighting measures 6. Accidental release measures 7. Handling and storage 8. Exposure controls/personal protection 9. Physical and chemical properties 10. Stability and reactivity 11. Toxicological information 12. Ecological information (non-mandatory) 13. Disposal considerations (non-mandatory) 14. Transport information (non-mandatory) 15. Regulatory information (non-mandatory) 16. Other information

## Slide 23: It is important that employees understand that information on a label does relate to information on the SDS. For instance, the Signal Word (“Danger” or “Warning”), as well as the Hazard Statement on a label are found in Section 2 of an SDS: Hazard Identification.

## Slide 24: Chemical companies and importers will have to re-format their SDS’s. Many have already begun this work.
Employees must have unencumbered access to SDS’s, without leaving their work area.

## Slide 25
RIPA Offers an SDS Yearly Subscription
(Through a 3rd-Party Provider)
24-Hour, 7-Days SDS Fax-on-Demand
Affordable, Convenient Service
OSHA-Compliant, GHS-Compliant
Member Signup is Each December for Upcoming Calendar Year

## Slide 26
Special Note 1: Combustible Dusts
Implications for Steel Shot
Combustible dust hazards must be addressed on GHS Labels and SDS’s.
Label elements are provided for combustible dust and include the signal word “Warning” and the hazard statement "May form combustible dust concentrations in the air".

## Slide 27
Special Note 2: Written HazCom Plans
OSHA regulations have required for many years a written Hazard Communication Plan.
RIPA has provided members a template; an easy-to-use format to “fill in the blanks”.
That template will be updated to reflect the new GHS label and SDS rules.
Updating is due June 1, 2016

## Slide 28
Certificate of Training
OSHA “HAZCOM 2012”
Globally Harmonized System (GHS)
Worker / Employee Training
Chemical Labels and Safety Data Sheets (SDS)
Trainee’s Name: _________________ Training Date: ____________
Employer: __________________________________________
Training Location (address) _______________________________________________
_______________________________________________