## Slide 1
RIPA Code of Operating Practice
Reprocessing and Recycling
Flexible Intermediate Bulk Containers (FIBCs)
As a member of the Reusable Industrial Packaging Association (RIPA), this company is committed to support the continuing effort to improve the industrial packaging industry’s responsible performance of its role in waste source reduction, recycling and responsible packaging management. We pledge to manage our business according to the following guiding principles. We:
Adhere to RIPA’s Code of Operating Practice for flexible intermediate bulk containers.
Recognize and respond to community concerns about industrial packaging disposal and the operations of industrial packaging reprocessing facilities.
Produce industrial packagings that are effective in safely containing all appropriate materials in transportation and storage.
Make health, safety and environmental considerations a priority in our planning for all existing and new processes.
Counsel packaging users on the safe manufacture, use, transportation, emptying, reuse, and recycling of industrial packagings.
Operate our plants in a manner that protects the environment and the health and safety of our employees and the public.
Work with others to resolve problems created by past industrial packaging disposal practices.
Participate with government and others in creating responsible laws, regulations, and standards to safeguard the community, workplace, and environment.
Promote the principles and practices of “Responsible Packaging Management” by sharing our experiences and offering assistance to others who produce, use, transport, or dispose of industrial packagings.
Foster the integrity and reputation of the industry by refraining from publishing knowingly false, misleading, or commercially disparaging statements or advertisements about our products and services, or the products and services of competitors.

## Slide 2
1.0 Basic Recommendation
Flexible Intermediate Bulk Containers (FIBCs) used for the transportation of hazardous materials that are remarked, mechanically altered, or that must be mechanically processed in any way to be able to meet the design-type tests, may not be reused without first being routinely maintained (per 49 CFR 180.350-352). Performance of any step of this process should be accompanied by performance of all associated steps. For example, if any element of routine maintenance is done (e.g., cleaning, then the entire process of routine maintenance should be completed in accordance with this Code. This is to assure that any reference to routine maintenance provides the filler of an FIBC with total packaging integrity.

## Slide 3
2.0 FIBC Reprocessing Firm
2.1 A business that properly reprocesses FIBCs for use in transporting hazardous or non-hazardous materials is one that possesses the necessary equipment and reprocesses FIBCs in accordance with all of the provisions described in this Code of Operating Practice. Where required, an FIBC reprocessing firm shall be registered or licensed by appropriate government authorities and shall mark reprocessed FIBCs intended for hazardous materials with the firm’s identification as its certification of regulatory compliance.
2.2 The reprocessing firm must maintain a documented quality control program.
2.3 The reprocessing firm shall encourage plant reviews during normal operating hours by any emptier or customer.
2.4 In addition to meeting the details of this Code of Operating Practice, the reprocessing firm should be in compliance with all federal, national, provincial and local government regulations pertaining to safety and health, and environmental protection.

## Slide 4
3.0 Definitions
3.1 “Intermediate Bulk Container” (IBC) is a U.S. DOT and international regulatory term for a type of packaging intended to transport hazardous materials (also referred to internationally as “dangerous goods”). IBCs are also widely used to transport non-hazardous, non-regulated materials.
3.2 A Flexible IBC (or “FIBC”) is an IBC constructed of woven plastic, plastic film, textile, or multiwall paper. Woven plastic FIBCs are typically constructed of polypropylene (PP). FIBCs range in size from 56 L (15 gallons) to 3,000 L (793 gallons); and have a minimum capacity of 50 kg (110 lbs).
3.3 “Bulk Bag” is a more general term, without regulatory meaning, typically taken to include FIBCs.
3.4 In addition to the term “bulk bag”, the term “FIBC” is in use to refer to the approximately 75% of FIBCs in non-hazardous service.
3.7 Regulatory authorities have assigned four codes to PP FIBCs which identify the packaging “design type” and are part of the full “UN mark” required on hazmat packagings and packages. The four design type codes for PP FIBCs are:
13H1 woven PP
13H2 woven PP w/coating
13H3 woven PP w/liner
13H4 woven PP w/coating and liner

## Slide 5
4.0 FIBC Reprocessing (“Routine Maintenance”)
4.1 U.S. regulations specify three levels of IBC reprocessing: routine maintenance, repair, and re-manufacturing.
4.2 FIBCs intended for reuse for hazardous materials may only be reprocessed with “routine maintenance” (a U.S. DOT regulatory term which includes “cleaning”, along with the possible replacement of non-integral components such as liners and closure ties; replacement parts must meet the “original manufacturer’s specifications”). FIBCs cannot be “repaired” or “remanufactured” for hazmat reuse.
4.3 The term “cleaning” in the regulations includes such measures as vacuuming and/or washing with water or a suitable water and detergent solution.
4.4 A routinely maintained FIBC must be marked in a durable manner (e.g. adhesive label) near the UN mark with the country where maintenance was conducted, and the name or authorized symbol of the party performing the routine maintenance. An example is presented here:
USA / M1234
4.5 After routine maintenance, it is the recommendation of this Code that reuse for Hazardous materials be restricted to the same product and the same prior filler. This will help minimize or eliminate concerns about the possible cross-contamination of a lading. Many FIBCs are used and reused for food grade material, and an extra level of care is warranted.
4.6 Alternatively, a routinely maintained unit could be used for hazardous waste provided the UN rating is sufficient for the waste’s level of hazard (e.g., X, Y, or Z, plus other ratings).

## Slide 6
5.0 Inspections
5.1 FIBCs are not subject to the 2 ½-year and 5-year inspection cycles that apply to composite, rigid, and metal IBCs. Therefore, there also are no requirements for keeping records of inspections.
5.2 Each FIBC must be visually inspected prior to first use and each reuse to ensure that:
5.2.1 The IBC is marked properly with its applicable UN performance mark. Marks that are missing, damaged or difficult to read must be restored or returned to original condition.
5.2.2 Proper construction and design specifications have been met.
5.2.3 Lifting straps, if used, are securely fastened to the IBC in accordance with the design type.
5.2.4 Seams are free from defects in stitching, heat sealing or gluing which would render the IBC unsafe for transportation of hazardous materials. All stitched seam-ends must be secure.
5.2.5 Fabric used to construct the IBC is free from cuts, tears and punctures. Additionally, fabric must be free from scoring which may render the IBC unsafe for transport.
5.3 U.S. DOT regulations require that all visual inspections of Section 5.2 also be conducted by the person who fills the FIBC

## Slide 7
6.0 Other Reuse
6.1 FIBCs deemed unsuitable for routine maintenance should be cleaned and/or washed, with all liners removed, cleaned and/or washed.
6.2 Factors that would render a used FIBC unsuitable for routine maintenance and reuse with hazardous materials include:
Broken straps
Open seams
Tears
UV damage
6.3 An FIBC without tears or leaks may nevertheless be suitable for reuse with certain non-hazardous materials, provided cross contamination is not a concern and provided the unit is fully cleaned.. For instance, non-hazardous, non-regulated waste material may be suitable for a used FIBC that is not being recertified for hazardous materials (i.e., not routinely maintained).

## Slide 8
7.0 Recycling
7.1 No polypropylene from a used FIBC may be used in the manufacture of plastic FIBCs intended for hazardous materials. Only production residues or regrind from the same manufacturing process can be used in producing FIBCs for hazardous materials (49 CFR 178.710(c)(6)).
7.2 Strict exclusion of scrapped hazmat FIBCs is necessary if the intent is make new non-hazardous FIBCs out of non-hazardous FIBC scrap.
7.3 These restrictions do not preclude the reuse of component parts such as fittings and pallet bases, provided such components have not been damaged in previous use.
7.4 Final regrind material may need to be separated according to FIBC manufacturer and color, with consideration given to prior contents. Regrind that is tainted (e.g., with paint, odor) should be managed separately.
7.5 Regrind which cannot be sold to an end user for any reason should be disposed of in compliance with all applicable federal, State and local laws and regulations.

## Slide 9
Here is where I could use some help from the experts.
What are the controls, the parameters, and the processes of turning FIBCs into regrind suitable for recycling? Are any residual solids “shaken” out? Vacuumed out? Will it depend on the location of the spout?
How are the used FIBCs prepared for grinding? Is the final grind in granular form, pellets, or both? Is one better than the other?
New FIBCs need to be constructed with additives that resist aging and degradation from UV radiation. Does that require additives to regrind? Or are those additives already present in the scrapped plastic?

## Slide 10
8.0 Collecting Used FIBCs
8.1 Before picking up used FIBCs, they should be collapsed, piled safely, and securely baled on pallets.
8.2 Prior to baling, all FIBCs that previously contained hazardous materials must be sufficiently cleaned of residue and purged of vapors to remove any potential hazard.
Unlike with drums, it is difficult to stipulate that used FIBCs with residues be shipped in the same manner as when they previously contained a greater quantity. Flexible IBCs will collapse when emptied, and it is not clear they could be properly closed in that state. Thus, it seems used hazmat FIBCs need to meet the criteria of section 6.2 before collecting and/or shipping to a recycler. If not, Superfund type liabilities could attach.

## Slide 11
9.0 Environmental and Employee Protection
9.1 Storage of FIBCs containing residues: Unreprocessed IBCs must be stored with all closures in place, and must be inspected periodically to assure no residual contents are leaking. All IBCs that are obviously unfit for reuse and/or re-certification should be rejected immediately and prepared for scrap in accordance with the preceding paragraphs.
9.2 All wastes generated in cleaning and washing must be managed in full compliance with applicable regulations governing such wastes.
9.3 Discharges of wastewater from the reprocessing plant to the environment or to the sewer system, and emissions to the atmosphere, must meet applicable water and air pollution regulations for the geographical area. Offensive odors must be minimized whether subject to government controls or not.
9.4 Exposure of employees to any chemicals in the workplace, including the contents of incoming FIBCs, must be reduced to the extent practicable. The use of effective personal protective equipment (PPE) is essential. The firm must have in place a written Hazard Communication Plan for employees, including federally mandated access to Material Safety Data Sheets (MSDS’s).
9.5 Employees must be trained in the proper performance of their jobs, including awareness of the Hazardous materials Regulations (HMR), their hazmat related functions, emergency response contingencies, and the hazard of any chemicals in the workplace.
9.6 Any employees that function as drivers adhere to the regulations of the U.S. Federal Motor Carrier Safety Administration (FMCSA). The firm shall adhere to rules on the qualification of drivers, including provisions relating to alcohol or other substance testing. Company vehicles shall be maintained in safe operating condition.
9.7 All practical precautions against fires must be implemented, including having adequate fire extinguishing capability, contingency planning, effective coordination with local emergency response authorities, and good housekeeping to minimize opportunities for ignition and to facilitate employee evacuation in emergencies.

## Slide 12
10.0 Public Statements and Advertising
10.1 Each RIPA member shall foster the integrity and reputation of the industrial packaging industry generally and the RIPA membership specifically by refraining from publishing knowingly false, misleading or commercially disparaging statements or advertisements.
10.2 Members’ public statements and advertisements shall not knowingly misrepresent fact or law, or create a negative impression or expectation about competitive products and services unless such statement or advertisement is based upon facts which are amenable to independent verification.